## Slide 1: Typhoon HIL internship
Typhoon HIL, Inc.
Nikola Fischer Čelanović
CEO
May 2023.
Teodora Mijović
tmijovic108@gmail.com
Juliano Grigulo
Mentor

## Slide 2: Agenda
Introduction - CHAdeMO
CAN bus protocol
Special features
Application demo
Simulation

## Slide 3: Introduction
“Charge de move” or “Ocha demo ikaga desuka” = “How about a cup of tea?”
First fast charging standard
Only DC charging supported
Communication via CAN bus
Master-Slave (BMS = Master, Charging station = Slave)
IEC 61851-24, Annex A
CHAdeMO standard

## Slide 4: Introduction
Different plugs - IEC 62196

## Slide 5: Introduction
1 – protective conductor (PE) = protective earth
2 – charging sequence signal (d1)
3 – not connected
4 – charging sequence signal (k)
5 – DC-
6 – DC+
7 – proximity detection (CP)
8 – CAN – High
9 – CAN – Low
10 – charging sequence signal (d2)
CHAdeMO pinout

## Slide 6: CAN bus protocol
CAN Setup is used to configure the CAN controllers settings for the chosen HIL device (exactly one CAN Setup component must exist in the model)
CAN Send and CAN Receive are similar, we can choose the CAN controller, define the message’s ID, length, and how it is going to be exchanged (on an event or on timer)
Messages (manually defined or imported DBC files)
CAN Setup, CAN Send, CAN Receive

## Slide 7: CAN messages
CHAdeMO communication essentially comprises 5 CAN messages
  3 for the vehicle side
  2 for the charging station
EV
  Message ID 0x100 - charge parameters
  Message ID 0x101 - calculated charge time
  Message ID 0x102 - signals for error marking
EVSE
  Message ID 0x108 - charge parameters
  Message ID 0x109 - signals for error marking
Messages IDs

## Slide 8: Circuit diagram

## Slide 9: Communication flow

## Slide 10: Special Features of CHAdeMO 2.0 and CHAdeMO 3.0
Dynamic control
  Charging station can increase or decrease ”available output current” during charging
V2L/V2H/V2V
  Vehicle to Load/Home/Vehicle
  Bidirectional charging
Output voltage range extended to 150-1500Vdc
Output current range extended to 0-600Adc
Output power range extended to 0-900kW
New ChaoJi connector
  Combines GBT (ChaoJi 1) and CHAdeMO (ChaoJi 2)
Changed and expanded communication
CHAdeMO 2.0
CHAdeMO 3.0

## Slide 11: Introduction to the project
Based on github project
State of machine
Links
  https://www.electricboxster.com/open-chademo
  https://github.com/Isaac96/CHAdeMOSoftware

## Slide 12: Charging process
Functions and states

## Slide 13: Advanced C Function block
Inputs
  Received messages from EVSE
Outputs
  Sent messages to EVSE
Logic of charging process
  chademo.cpp

## Slide 14: Simulation
Steps
1. Close contactor ”Charging cable” – physical connection between EV and EVSE
2. Close contactor ”d1” – signal IN1 goes high (signalizing us that connection is made)
3. Send EV’s parameters to EVSE (for example: battery specifications, charging time..)
4. Close contactor ”d2” – signal IN2 goes high (battery terminals are connected to the grid, charging starts)

## Slide 15: Conclusion
Communication between EV and EVSE based on CHAdeMO standard (EV side)
Next Steps
  Package manager – CHAdeMo EV component
  Test with Vector CANoe
  CHAdeMo 2.0
  GB/T

## Slide 16: Thank you for your attention!
May 2023.
Teodora Mijović
tmijovic108@gmail.com